## Slide 1: RGB 5x5 Convolution Engine on FPGA
Architecture, Verification, and Timing Closure Summary

## Slide 2: System Goal
Runtime-programmable 5x5 RGB convolution on streaming input
AXI-Stream datapath + AXI-Lite kernel control
Simulation-first signoff before board deployment

## Slide 3: Dataflow Architecture
AXI-Stream In
line_buffer_4
kernel_loader
mac_array_25x3
AXI-Stream Out
AXI-Lite Control: axi_lite_kernel_ctrl

## Slide 4: Numeric and Pipeline Details
Pixel: RGB888, Coeff: signed 16-bit, Accumulator: signed 48-bit
Fixed-point normalization: KERNEL_Q = 8
MAC pipeline staged for timing closure and stable throughput
Output valid delayed by internal MAC pipeline stages

## Slide 5: Verification and Timing Status
Regression PASS: identity5, gaussian5, sharpen5, emboss5, laplacian5
Timing clean at 40 MHz (25 ns)
Stretch points 50/60 MHz still pending closure
Next gate: AXI backpressure hardening + SAIF confidence uplift

## Slide 6: Roadmap to Final Demo
Gate F hardening: randomized backpressure and interface stress
Power confidence uplift with realistic SAIF activity
Reproducible benchmark matrix (resolution x kernel)
Seminar package: waveform proofs, timing table, live demo